## Slide 1: Hardware Software Platforms Project Presentation
DE1-Temperature sensor
Luypaert Charlotte
Vanvilthoven Julien
Charlotte.LUYPAERT@student.umons.ac.be
Julien.VANVILTHOVEN@student.umons.ac.be

## Slide 2: Plan
Project description
I2C explanations
Driver state machine and simulation
Application simulation
Driver and application simulation
Simulation on the oscilloscope
Video
Demonstration
Sources

## Slide 3: Project description
Goal: Learn how to manage a temperature sensor on an FPGA (Field-Programmable Gate Array)
Use of the Quartus software to implement our project
Make simulations to be sure everything works properly before sending the code on a chip
Implement our code on the Altera Cyclone V SoC.

## Slide 4: I2C (inter integrated circuit)
Goal: Making communication between electronic components with three wires:
  Data signal: SDA
  Clock signal: SCL
  Electric reference signal:Ground

## Slide 5: i2C
Takeover of the bus :
  Before data transmission : SCL and SDA at 1
  Start condition : SCL at 1 and SDA at 0
  Stop condition : SCL at 1 and SDA at 1
  Bus freetaking controlcircuit becomes Master and generates clock signal.

## Slide 6: i2C
Byte transmission
Master
Slave
SDA
SCL

## Slide 7: i2C
Adresses transmission
  Register address
  Device address
  Data
  The address is defined on seven bits. The eighth bit is the R/W wich determines if the master wants to read or write.

## Slide 8: State-machine of the driver
Found on: https://www.digikey.com/eewiki/pages/viewpage.action?pageId=10125324

## Slide 9: Driver simulation
The simulations have been done on ModelSim
To see if our code works well, we put a fake data (d). Otherwise we can’t see if the data is read or not.

## Slide 10: Application
Temperature sensor
VHDL Code based on PIC Code
Read of temperature on the leds (the eight most significant bits are read)

## Slide 11: Application simulation
The simulations have been done on ModelSim

## Slide 12: Driver and application Simulation
Assembly of the two codes: the driver and the application

## Slide 13: Simulation on the oscilloscope
To check the I2C data frame, we connected the SDA and the SCL on the oscilloscope
Setting the resolution
Device address
Registers address
Reading the temperature
Reading the 2 bytes
Writing the 0x00

## Slide 14: Assembly on breadboard
The two pins, SCL and SDA are common collector. To polarize them, we have to add two resistors:
One between VDD and SCL
One between VDD and SDA

## Slide 16
A short demonstration

## Slide 17
Conclusion

## Slide 18: Sources
https://www.les-electroniciens.com/sites/default/files/cours/cours_i2c.pdf
I2C Introduction au bus I2C, Camille Diou
url:https://www.les-electroniciens.com/sites/default/files/cours/cours_i2c.pdf